## Slide 1
CCE 313 – Computer Networks: IP Subnetting
Presented By: Nazmus Sakib
Student ID: 2102066
B.Sc. CSE – 5th Semester
Date: 24/11/2025
Reg: 10193

## Slide 2
Introduction to IP Subnetting
Introduction
IP Subnetting is the strategic division of a large network into smaller, more manageable logical networks. This process is fundamental for the efficient organisation and allocation of IP addresses within any robust network infrastructure.
It serves as a critical tool for network administrators to optimize network performance and resource utilization.

## Slide 3
IP Subnetting is used to split a large network into smaller logical sub-networks. Without subnetting, large networks face broadcast storms, inefficient IP usage, congestion, and weak security separation. Subnetting helps optimise performance and ensures better management of IP addresses.
Problem Statement
Without proper subnetting, large networks are prone to
several critical issues:
Broadcast storms: Excessive broadcast traffic can
overwhelm network devices.
IP wastage: Inefficient allocation leads to unused IP addresses.
Congestion: Unnecessary traffic causes network slowdowns.
Lack of security segmentation: Difficulty in isolating
vulnerable sections.
Importance
Implementing IP subnetting profoundly enhances
network performance, significantly reducing broadcast traffic and bolstering security segmentation across the network. This results in a more stable, secure, and efficient operating environment.

## Slide 4
IP Address Structure & Subnet Mask
IPv4 Structure
An IPv4 address is a 32-bit numerical label assigned to devices connected to a computer network. It is conventionally represented in dot-decimal notation.
It comprises two main parts: a Network part and a Host part.
Example: 192.168.10.5
Subnet Mask
The subnet mask is a 32-bit number that distinguishes the network part of an IP address from the host part. It effectively determines how many bits are used for the network identification.
Examples:
255.255.255.0 (/24) – A common mask for smaller networks.
255.255.255.192 (/26) – A mask indicating more subnets.
255.255.255.252 (/30) – Often used for point-to-point links.
Host Bits
Specifies individual device addresses
Subnet Bits
Defines subnetwork segmentation and mask
Network Bits
Identifies the routing network portion

## Slide 5
An IPv4 address has 32 bits divided into network and host portions. The subnet mask indicates how many bits belong to the network. For example, /24 uses 24 bits for the network. When we create subnets, we adjust this mask to allocate bits differently.

## Slide 6
How Subnetting Works
Borrow Bits
Subnetting fundamentally involves 'borrowing' bits from the host portion of an IP address. These borrowed bits are then used to create additional network addresses, effectively segmenting the larger network.
Create Subnets
By borrowing bits, we create multiple, smaller, independent networks, known as subnets. Each subnet operates as its own broadcast domain, reducing overall network traffic and improving efficiency.
Apply Formulas
Specific formulas are used to calculate the number of subnets and the number of usable hosts within each subnet, ensuring precise network planning.
Number of Subnets
Calculated as 2ⁿ, where 'n' represents the number of borrowed bits from the host portion. This directly determines how many subnets can be created.
Hosts per Subnet
Determined by 2ʰ – 2, where 'h' is the number of remaining host bits. The subtraction of two accounts for the network address and the broadcast address, which are not assignable to hosts.

## Slide 7
Subnetting works by borrowing bits from the host portion. If we borrow n bits, we get 2ⁿ subnets. If we have h remaining host bits, we get 2ʰ minus 2 usable hosts. For example, turning /24 into /26 involves borrowing 2 bits, which creates 4 equal-sized subnets.
Example: Transitioning from /24 to
/26
By borrowing 2 bits from the host portion of a /24 network, we generate 4 distinct subnets.
This provides a granular control over network segmentation and IP allocation.

## Slide 8
Subnetting Example (Worked Solution)
Given:
192.168.10.0/24
Required:
4 subnets
Step 1: Borrow Bits
To achieve 4 subnets, we need to borrow 2 bits (since 2² = 4). This changes the subnet mask from /24 to /26.
Step 2: Determine Subnet Ranges
Each subnet will have a block size of 64 addresses (2^(32-26) = 2^6 = 64). The ranges are as follows:
192.168.10.0 – 192.168.10.63
192.168.10.64 – 192.168.10.127
192.168.10.128 – 192.168.10.191
192.168.10.192 – 192.168.10.255
Each Subnet:
Usable hosts: 62 (64 total addresses - 2 for network/broadcast)
Broadcast address: Always the last address in each range.

## Slide 9
Here is a practical subnetting example. For the network 192.168.10.0/24, we need 4 subnets. By borrowing 2 bits we get a /26 mask. This gives us four subnets, each providing 62 usable host addresses. These ranges are clearly separated and help organise networks efficiently.

## Slide 10
Analysis & Practical Implications
Large Organisations
Essential for segmenting departments and improving network security and performance.
Universities & Campus Networks
Manages vast numbers of devices and users across different faculties and dormitories.
ISPs
Crucial for allocating IP addresses to millions of customers efficiently and managing network traffic.
VLAN-based Networks
Integrates seamlessly with VLANs to create logical broadcast domains, further enhancing network control.
Routers and Routing Tables
Fundamental for routers to correctly forward packets between different subnets, maintaining efficient data flow.
Key Benefits of Subnetting
Efficient IP Address Usage
Minimises wastage of valuable IP addresses, ensuring resources are optimally utilised.
Smaller Broadcast Domains
Reduces network congestion and enhances performance by limiting the scope of broadcast traffic.
Improved Performance
Leads to faster network response times and greater overall operational efficiency.
Better Security Segmentation
Allows for the isolation of network segments, preventing security breaches from spreading across the entire network.

## Slide 11
Thank
You